## Slide 1: Adaptive Multi-Client Antenna Orientation Optimization for Wireless APs.

## Slide 2: Background of the Invention (What is the problem being solved and how was the problem previously solved?):
Most commercially available Wi-Fi access points use fixed antenna orientations that cannot be adjusted after installation. Consequently, the antenna radiation pattern remains the same regardless of the deployment environment. However, the optimal antenna orientation depends on the physical layout of the building and the client locations. For example, in a multi-story home with a basement, an AP installed on the second floor should direct more energy downward, whereas an AP installed in the basement should provide stronger upward radiation. Because the antenna orientation is fixed, the resulting Wi-Fi coverage is often not optimized for the installation environment, leading to reduced coverage and performance.

## Slide 3: Known Prior Art
Some patents propose to optimize antenna direction toward devices but they do not propose the AP learning every client's preferred orientation over time or do not take into account client traffic need to know what clients to prioritize. They optimize mathematically from channel estimates. Prior work do not propose calibration sweep.

## Slide 4: Description of the Invention
The invention optimizes the antenna orientation of a Wi-Fi access point using motorized antennas to improve the overall user experience throughout the home. The optimization is performed in several steps.
1. Wireless channel characterization by rotating antennas (Calibration): The AP performs a calibration sweep by rotating the antennas through different orientations while collecting performance metrics for each associated device. This process determines the antenna orientations that provide the best performance for each device.
2. Device characterization: The AP identifies the type of each connected device (e.g., IoT device, PC, laptop, TV, phone, gaming console) and collects information about its traffic characteristics.
3. Device prioritization: Each device is assigned a priority based on its class and traffic requirements. Devices that benefit from high throughput and low latency, such as gaming consoles, phones, TVs, and PCs, receive higher priority, while devices with limited bandwidth or latency requirements, such as thermostats or other IoT devices, receive lower priority.
4. Antenna orientation optimization: Using the calibration results and the assigned priorities, the AP determines the antenna orientation that provides the best overall performance for all connected devices, while favoring the devices that have the greatest impact on the user experience. Algorithms could be based on weighted utility maximization, proportional fairness. Reinforcement learning can be used if the AP is capable of learning over time from traffic patterns and device movement – see below)
Additional steps for further optimization include
5. Learning: The AP repeats the calibration periodically or when significant changes are detected in the network (for example, a new device joins, a device moves, or traffic patterns change). The AP builds a history of the preferred antenna orientations for each device.
6. Prediction: For mobile devices such as phones and laptops, the AP learns recurring locations and usage patterns. Based on this history, the AP can proactively adjust the antenna orientation before or during periods of expected high traffic, reducing the need for a full calibration sweep.
Notes: Score(angle) = Σ weight(client) × performance(client, angle)
Where performance could include:
throughput latency RSSI/SNR packet error rate MCS stability
A practical scoring function could be:
Score(angle) = Σ Wi × [a × throughput_i(angle) - b × latency_i(angle) - c × packet_loss_i(angle)]
Where:
Wi = device priority weight
  gaming console: high
  TV: high
  laptop: medium/high
  phone: medium/high
  thermostat: low
a, b, c = tuning factors
i = each client
Then the AP selects:
best_angle = angle with maximum Score(angle)

## Slide 5: Description of the Invention - Questions
The invention optimizes the antenna orientation of a Wi-Fi access point using motorized antennas to improve the overall user experience throughout the home. The optimization is performed in several steps.
1. Calibration: The AP performs a calibration sweep by rotating the antennas through different orientations while collecting performance metrics for each associated device. This process determines the antenna orientations that provide the best performance for each device.
  How to reduce the number of position for the sweep
  What kpis to record (RSSI, collision, PER, ???)
2. Device characterization: The AP identifies the type of each connected device (e.g., IoT device, PC, laptop, TV, phone, gaming console) and collects information about its traffic characteristics.
  Device category based on DHCP hostname/fingerprinting, device MAC address, DNS, mDNS
  Traffic characteristic based on DPI, AI to classify audio, video, gaming and throughput requirement (other KPIS?)
3. Device prioritization: Each device is assigned a priority based on its class and traffic requirements. Devices that benefit from high throughput and low latency, such as gaming consoles, phones, TVs, and PCs, receive higher priority, while devices with limited bandwidth or latency requirements, such as thermostats or other IoT devices, receive lower priority.
4. Antenna optimization: Using the calibration results and the assigned priorities, the AP determines the antenna orientation that provides the best overall performance for all connected devices, while favoring the devices that have the greatest impact on the user experience. Algorithms could be based on weighted utility maximization, proportional fairness. Reinforcement learning can be used if the AP is capable of learning over time from traffic patterns and device movement – see below)
  Antena orientation – example of calculation
  An alternative is to have multiple antennas in the AP (e.g., 16) and select best antenna to use – replacing the “motorized antenna approach”
Additional steps for further optimization include
5. Learning: The AP repeats the calibration periodically or when significant changes are detected in the network (for example, a new device joins, a device moves, or traffic patterns change). The AP builds a history of the preferred antenna orientations for each device.
6. Prediction: For mobile devices such as phones and laptops, the AP learns recurring locations and usage patterns. Based on this history, the AP can proactively adjust the antenna orientation before or during periods of expected high traffic, reducing the need for a full calibration sweep.
  AI based
Notes: Score(angle) = Σ weight(client) × performance(client, angle)
Where performance could include:
throughput latency RSSI/SNR packet error rate MCS stability
A practical scoring function could be:
Score(angle) = Σ Wi × [a × throughput_i(angle) - b × latency_i(angle) - c × packet_loss_i(angle)]
Where:
Wi = device priority weight
  gaming console: high
  TV: high
  laptop: medium/high
  phone: medium/high
  thermostat: low
a, b, c = tuning factors
i = each client
Then the AP selects:
best_angle = angle with maximum Score(angle)

## Slide 6: Diagrams: to do

## Slide 7: 1. Wireless channel characterization by rotating antennas
By rotating one or more AP antennas, AP could characterize (step 1) angle of arrival (AoA) and other propagation channel characteristics from each client device. Based on such AoA information, AP could optimize antenna(s) orientation to improve coverage and performance (step 4)
Different methods could be designed under various conditions
  Knowledge of client device locations (fixed or mobile)
  Knowledge of indoor floorplan and location of furniture/obstacle in the environment
  AP antenna only rotate in one direction (one motor or one axial), two directions (two motors or two axials), three directions (three motors or three axials)
    @Shizen and @Hao, please draw a diagram with one AP, four antennas, and the three axials of one example antenna…
SAGE/MUSIC and other algorithms can be leveraged or modified to characterize AoA by comparing relative phase and amplitude difference when AP antennas rotate (assuming in a static channel)
Potential simulation could be built to demonstrate AoA characterization results and AP performance improvement (hold on for any action)

## Slide 8
Calibration and sensing: (Find fixed device) (Pre-knowledge) Optimization: (Best angle for fixed devices; leverage fixed and mobile; how to follow mobile)
(Fixed/Mobile) One axial：
Two axials：
Three axials：
Mechanical pattern